#### Read register for Pins
#### U3:
The U3 uses flex pins, meaning a pin can be either an analog input, digital input or digital output. They can also be counters or timers depending on configuration. For analog input, and digital I/O the pin mapping is:
I/O Pin:	Ch:	I/O Pin:	Ch:	I/O Pin:	Ch:
FIO0 (AIN0)	0	EIO0 (AIN8)	8	CIO0	16
FIO1 (AIN1)	1	EIO1 (AIN9)	9	CIO1	17
FIO2 (AIN2)	2	EIO2 (AIN10)	10	CIO2	18
FIO3 (AIN3)	3	EIO3 (AIN11)	11	CIO3	19
FIO4 (AIN4)	4	EIO4 (AIN12)	12
FIO5 (AIN5)	5	EIO5 (AIN13)	13
FIO6 (AIN6)	6	EIO6 (AIN14)	14
FIO7 (AIN7)	7	EIO7 (AIN15)	15

Note that the CIO pins are digital only. You should only use a pin for one of the three uses, so be careful not to use the same channel number for separate analog input, digital input or digital output channels.
If you enable timers or counters, they will use up the appropriate number of pins starting with FIO0. This does not change the rest of the channel numbers. So, if you have two timers enabled, they will be on FIO0 and FIO1. FIO2 remains channel 2 to DAQFactory. Of course if you use the pin offset option for timers and counters, the timers might be on different pins, but even the mapping of DAQFactory channel numbers to pins remains the same.

1.39398193359375,
 1.3949823379516602,
 0.014410018920898438,
 1.3944520950317383,
 0.4829981327056885,
 0.39291971921920776,
 0.38993701338768005,
 0.43885374069213867,
 0.38576117157936096,
0.34758225083351135,
 0.39590245485305786,
 0.33923062682151794,
 0.31954461336135864]
https://labjack.com/support/software/api/modbus/ud-modbus
https://labjack.com/support/datasheets/u3/hardware-description/ain/analog-input-connections/unconnected-inputs